## Slide 1: Recent progress on greenhouse gas measurements at Mt. Lulin and Dongsha Island, Taiwan
Chang-Feng Ou-Yang1, Neng-Huei Lin1, Jia-Lin Wang2, Russell C. Schnell3
1Department of Atmospheric Sciences, National Central University
2Department of Chemistry, National Central University
3NOAA/ESRL/GMD

## Slide 2: History of baseline GHG measurements in Taiwan
2006 August
Mt. Lulin joined
NOAA/CCGG
Typhoon Morakot
2009 August
2010 March
Dongsha joined
NOAA/CCGG
CFC/VOC measurements
started at Lulin
2013 November
2011 February
In-situ measurements of
CO2 and CH4 started
at LABS by Picarro
2015 April
Picarro G1301
stopped
Mt. Lulin opened
2006 April
Picarro restored
2016 September
2017
New sites/
instruments

## Slide 3: Locations
Taiwan
China
Japan
Korea
Vietnam
Philippines
Dongsha Island (DSI)
Lulin Mountain (LLN)
Thailand
Lulin:
23.47°N, 120.87°E; 2862 m a.s.l.
(Free troposphere)
Dongsha:
20.70°N, 116.73°E; 5 m a.s.l.
(Sea-level)

## Slide 4: Mt. Lulin
LLN
Taiwan
LLN
In-situ measurements of gases:
O3, CO, SO2, CO2, CH4
Flask air sampling (Weekly):
CO2, δ13C_CO2, δ18O_CO2, CH4, N2O, SF6, CO, H2,
CFCs, VOCs
(23.47°N, 120.87°E, 2862 m a.s.l.)

## Slide 5: Dongsha Island
Flask air sampling (Weekly):
CO2, δ13C_CO2, δ18O_CO2, CH4, N2O, SF6, CO, H2
DSI
(20.70°N, 116.73°E, 5 m a.s.l.)

## Slide 6: CO2
DSI:
404.60±5.28 ppm
(+2.10 ppm yr-1)
LLN:
402.61±3.11 ppm
(+2.69 ppm yr-1)
2015
Notes: MLO growth rate = 2.21 ppm yr-1

## Slide 7: CH4
DSI:
1894.4±55.0 ppb
(+6.4 ppb yr-1)
LLN:
1877.2±36.7 ppb
(+6.9 ppb yr-1)
2015

## Slide 8: N2O
DSI:
329.3±0.6 ppb
(+1.1 ppb yr-1)
LLN:
329.2±0.6 ppb
(+0.9 ppb yr-1)
2015

## Slide 9: Cluster analysis of backward trajectories at Dongsha Island
Winter monsoon
27%
31%
19%
16%
7%

## Slide 10: Cluster analysis of backward trajectories at Mt. Lulin
4%
13%
40%
11%
32%

## Slide 11: Frequency
from Pacific
from Southeast Asia
from East China
from South China Sea

## Slide 12: Contributions
 | N | % | CO2 (ppm) | CH4 (ppb) | N2O (ppb)
L1 (Pacific) | 225 | 32% | 389.2±8.9 | 1832±34 | 324.8±2.5
L2 (South China Sea) | 278 | 40% | 390.6±7.6 | 1833±37 | 324.8±2.4
L3 (East China) | 77 | 11% | 395.3±12.2 | 1875±31 | 326.9±3.0
L4 (Southeast Asia) | 92 | 13% | 393.1±6.9 | 1859±25 | 325.2±2.2
L5 (Others) | 30 | 4% | 393.9±6.4 | 1860±28 | 325.3±2.2
L1
L2
L3
L4
L5

## Slide 13: Cluster analysis of backward trajectories in periods
Period 1
(N = 162)
Joined NOAA/CCGG
2006 August
Typhoon Morakot
2009 August
Period 2
(N = 161)
Period 3
(N = 173)
2012 September
2016 March

## Slide 14
L2
L2
L2
L4
L4
L4
L1
L1
L1
L3
L3
L3
L5
L5
L5
Period 1
Period 2
Period 3
CO2 (ppm) | CH4 (ppb) | N2O (ppb)
∆2.7±5.2 | ∆22±24 | ∆0.8±1.3
CO2 (ppm) | CH4 (ppb) | N2O (ppb)
∆1.2±7.6 | ∆12±15 | ∆0.2±1.0
L3 (15%)
L3 (20%)

## Slide 15
Period 2
Period 3
Total Spatial Variance
Total Spatial Variance

## Slide 16: Air masses from East China
Period 2
Period 3

## Slide 17: In-situ measurements of CO2 and CH4 at Mt. Lulin
Mean difference: 0.59±1.61 ppm CO2
Mean difference: 0.24±8.61 ppb CH4

## Slide 18: Inter-comparisons of CO2

## Slide 19: Inter-comparisons of CH4

## Slide 20: Diurnal variations of CO2 and CH4

## Slide 21: Mountain-valley breezes
3000 m
1500 m
0 m
Lulin
Daytime
Nighttime
Sun

## Slide 22: Diurnal spectrum

## Slide 23: Future Plan: GHG Network
Taiwan
China
Japan
Korea
Vietnam
Philippines
Dongsha Island (DSI)
Mt. Lulin (LLN)
Thailand
Taiping Island
Lanyu Island
Mt. Bamboo
Mt. Yushan
(Mt. Lulin)

## Slide 24: Taiping Island
10.37°N, 114.37°E

## Slide 25: Mt. Yushan
Yushan weather station (3845 m a.s.l.)
9.2 km away from Mt. Lulin
983 m higher than Mt. Lulin
Mt. Yushan (3952 m a.s.l.)

## Slide 26: Lanyu Island
22.04°N, 121.55°E, 324 m a.s.l.
CO2 measurement since 1995

## Slide 27: Mt. Bamboo
25.19°N, 121.55°E, 1103 m a.s.l.
Mt. Bamboo
View from the site

## Slide 28: Summary
Clear increasing trends for CO2, CH4, and N2O were found.
Annual mean of CO2 at Mt. Lulin and Dongsha Island exceeded 400 ppm in 2015 and 2014, respectively.
Distinguished seasonal and diurnal cycles for CO2 and CH4 were observed.
Cluster analysis of trajectories has shown that the air masses originated from East China are found with highest levels of greenhouse gases.
4 new monitoring sites for GHGs proposed.

## Slide 29: Acknowledgements
NOAA/GMD
Contact: cfouyang@cc.ncu.edu.tw